## Slide 1: Analysis of an autoencoder-based approach
BIWO - 08 Project Work
Room 02-001, August-Bebel-Str. 30 // August 11, 2022
By Anvar Mohamed Aslam Sha
for determining the configuration
of embedded obstacles

## Slide 2: Motivation and goal
  Major investigations had been conducted on the wave scattering behaviour of fibre-reinforced materials.
  These fibers are built-up from numerous filaments of materials leading to a layered inner structure of the multi-filament yarns.
  Stress waves can be focused within the regions of heterogeneity in composite material.
  Aim is to implement an autoencoder-based approach to automatically determine the geometric parameters of composite materials.
The elliptical shape of the
multifilament yarn

## Slide 3: Problem configuration

## Slide 4: Problem configuration
Based on this specific inner structure of the yarns, a 2D-mechanical model was developed.
By projecting the complex 3D nature of the problem into a so-called plane of observation model was simplified.
The normal wave gets scattered by the obstacle.
The amplitude response spectra was determined by obstacle’s configuration.
In the experimental data dimensionless frequency stiffness, density, etc are the obstacle configuration and normalized amplitudes at various measuring points are wave response spectra.
Simplified 2D model

## Slide 5: 2D mechanical model
Core
Interphase
Normal waves
Scattered waves
Amplitude measuring points
Matrix

## Slide 6: Artificial neural networks

## Slide 7: Artificial neural networks
  The term neurons in neural networks, which is an analogy to the biological neurons, are presented as conceptual components for circuits that could perform computational tasks.
  This idea of neuron processing was implemented on multilayer perceptron.
Dendrites
Nucleus
Cell body
Axon
Node
Axon
terminal

## Slide 8: Two-layer multilayer perceptron
Input layer

## Slide 9: Two-layer multilayer perceptron
Input layer
Hidden layer

## Slide 10: Two-layer multilayer perceptron
Input layer
Hidden layer
Output layer

## Slide 11: Neuron processing
Input neurons
Input
Output
o
Weighted sum
Activation function
Output neuron
Weights
ReLu

## Slide 12: Computation graphs

## Slide 13: Computation graph
Computational graphs are a type of graph that can be used to represent mathematical expressions.
In general, the computational graph is a directed graph that is used for expressing and evaluating mathematical expressions.
These can be used for two different types of calculations:
    Forwardpass
    Backwarpass

## Slide 14: Computation graph
Bias
Two inputs
but only one sample
i.e. scalar inputs

## Slide 15: Computation graph
Weighted sum

## Slide 16: Computation graph
Weighted sum
Sigmoid
activation function

## Slide 17: Forwardpass
Forward pass
Weighted sum
Sigmoid
activation function
Squared error
For multiple samples mean of the
squared errors is optimized

## Slide 18: Backwardpass
Backward pass
Forward pass

## Slide 19: Backwardpass
Backward pass
Forward pass

## Slide 20: Gradient descent algorithm
Global minima
Local minima
Gradient descent update rule
Where, is the learning rate.
It controls the response of the updates.
One cycle of forward and backward pass
is called an epoch

## Slide 21: Normalization
Large ranged inputs
Nominal ranged inputs

## Slide 22: Convolutional neural networks

## Slide 23: 1D Convolution neural networks
Instead of directly passing the inputs to the input neurons of the multipayer perceptron, convolution is performed.
Convolutional neural networks or CNNs have three layer.
        Covolutional layer:
        Dot product of kernels and the input signal to create convolved 2D array.
        Pooling layer:
        Extracts max value from each sliding action.
        Fully connected layer:
        Converts convolved 2D array into a 1D array before feeding it into multilayer
        perceptron.

## Slide 24: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
1D Array
2D Array
x
x
x
+
Calculates dot product of the input signal and kernel

## Slide 25: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
x
x
x
+
1D Array
2D Array
Sliding action of the kernel

## Slide 26: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
x
x
x
+
1D Array
2D Array
Kernel slides with a stride of 1 unit

## Slide 27: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
x
x
x
+
1D Array
2D Array
10x1
3x1
8x1

## Slide 28: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
54
28
0
0
"Same” padding
2D Array
1D Array
2D Array
x
x
+
x

## Slide 29: Convolution layer
3
7
6
1
4
5
1
3
4
6
1
4
6
64
37
34
47
30
25
37
55
Input
Kernel
Feature map
54
28
0
0
"Same” padding
2D Array
1D Array
2D Array
x
x
+
x

## Slide 30: Convolution layer
3
7
6
1
4
5
1
4
Input
Kernel
Feature map
31
10
24
+
x
x
1D Array
2D Array

## Slide 31: Convolution layer
3
7
6
1
4
5
1
4
Input
Kernel
Feature map
31
10
24
+
x
x
1D Array
2D Array
Kernel slides with a stride of 2

## Slide 32: Convolution layer
3
7
6
1
4
5
1
4
Input
Kernel
Feature map
31
10
24
+
x
x
1D Array
2D Array

## Slide 33: Convolution layer
Input
Kernel
Feature map
6x1
2x1
3x1
2D Array
Feature
maps
1D Array
3
7
6
1
4
5
1
4
31
10
24
+
x
x

## Slide 34: Max pooling
Input/
Feature
map
64
37
34
47
30
25
37
55
54
54
64
37
64
47
55
Max pool filter
Global pooling
9x1
3x1
3x1

## Slide 35: Max pooling
Input/
Feature
map
64
37
34
47
30
25
37
55
54
34
47
30
64
47
55
Max pool filter
Global pooling
9x1
3x1
3x1

## Slide 36: Max pooling
Input/
Feature
map
64
37
34
47
30
25
37
55
54
25
37
55
64
47
55
Max pool filter
Global pooling
9x1
3x1
3x1
Downsampling

## Slide 37: Fully connected layer
2D Array
Feature maps/
Global pooling
5 x 64

## Slide 38: Fully connected layer
2D Array
Flattening
5 x 64

## Slide 39: Fully connected layer
2D Array
5 x 64
320 x 1
Flattening
1D Array
Fully Connected Layer is simply, feed forward neural networks.
The input is flattened and then fed into the fully connected layer.

## Slide 40: Machine learning model
Python 3.10
Matplotlib
Keras
Tensorflow
Scikit-learn
Normalization
Training validation split
CNN Model
Nvidia
GTX 960m
80% of the input data
Is trained and remaining
Is kept for validation.

## Slide 41: Estimation of normalized amplitudes

## Slide 42: Simplified training
The multi-output regression problem of estimating normalized amplitude at different measuring points is simplified to a 2D problem.
CNN model is trained on 1D input, dimensionless frequency to predict 1D output, amplitude.
Loss (MSE) is calculated at each epoch.

## Slide 43: Simplified training

## Slide 44: Simplified training

## Slide 45: Simplified training
Even though the model was able to learn during the training, the results were still poor.
Predicted and target values of the normalized amplitude are compared by calculating the mean absolute percentage error.

## Slide 46: Simplified training

## Slide 47: Simplified training

## Slide 48: Simplified training
For further analysis, the predicted and target amplitudes are plotted against the dimensionless frequency.

## Slide 49: Simplified training

## Slide 50: Simplified training
As observed, the approximated function
is unable to map the input appropriately.

## Slide 51: Patchwise training
Dimensionless Frequency
1.4967
1.6633
1.8300
1.9873
50.8840
50.9988
51.1655
51.3321
1.4967
1.6633
1.8300
1.9873
19.5935
19.6641
19.8308
19.9975
For example
patch size
of 0 to 20

## Slide 52: Patchwise training
Dimensionless frequency
1.4967
1.6633
1.8300
1.9873
19.5935
19.6641
19.8308
19.9975
Instead of simplifying the forward approach, multi-output regression is performed i.e. amplitude at multiple points are estimated simultaneously.
Number of learning parameters greatly reduced.
Less processing time.

## Slide 53: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
In conjunction to the patchwise training
similarity analysis is also performed for
Multi-output regression problem.

## Slide 54: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
0.74%

## Slide 55: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
1.52%

## Slide 56: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
20.08%

## Slide 57: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
0.79%

## Slide 58: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
10.14%

## Slide 59: Similarity analysis
Normalized Amplitudes
0. 75885
0. 75325
0. 74724
0. 82965
0. 82898
0. 83324
0. 90754
0. 87578
0. 90121
0. 91129
20.98%
Samples with the least percentage
difference are removed from
the training set.

## Slide 60: Patchwise training
Now the machine learning model is trained with 119 samples and patch size of dimensionless frequency in the range of 3 to 3.05.
Loss (MSE) is calculated at each epoch.

## Slide 61: Simplified training
Predicted and target values of the normalized amplitude are compared by calculating the mean absolute percentage error.

## Slide 62: Simplified training

## Slide 63: Simplified training

## Slide 64: Simplified training
For further analysis, the predicted and target amplitudes are plotted against the dimensionless frequency.

## Slide 65: Simplified training

## Slide 66: Simplified training
As observed, the model is able to produce
a good approximation of the function.

## Slide 67: Estimation of obstacle configuration

## Slide 68: Patchwise training
Now we estimate obstacle configuration from the normalized amplitudes.
The machine learning model is kept the same.
Loss (MSE) is calculated at each epoch.

## Slide 69: Simplified training
Predicted and target values of the obstacle configuration and , are compared by calculating the mean absolute percentage error.

## Slide 70: Simplified training

## Slide 71: Simplified training

## Slide 72: Simplified training
For further analysis, the predicted and target configurations are plotted against the dimensionless frequency .

## Slide 73: Simplified training

## Slide 74: Simplified training
As observed, the model is able to produce
a good approximation of the function.

## Slide 75: Conclusion
An already developed 2D-mechanical model which was based on the inner structure of the multi-filament was studied.
To determine the configuration of embedded obstacle from amplitude response spectra, an autoencoder-based approach was carried out using convolutional neural networks.
For further improvement of the machine learning model, two novel strategies were developed, patchwise training and similarity analysis.
Thus, a numerical method alternative to the analytical solution of the 2D-mechanical model was developed.

## Slide 76: Thank you